## Slide 1
NCC → KCF Handover Pipeline
Initial acquisition via NCC; real-time tracking via KCF
KCF Visual Tracker RTL IP Core
FRAME
STAGE
OUTPUT
METRIC
Frame 1
Training
Frame 2
Acquisition
Frame 3+
Tracking
KCF TRAINING
• Hann window the patch • 2D-FFT → compute α̂ • Store α̂ into on-chip ROM
NCC ACQUISITION
• Cross-correlate template • Normalise scores → map • Peak → initial (r, c)
KCF DETECTION
• Hann window the patch • FFT → R̂ = X̂·Ẑ·α̂ • IFFT → argmax (Δr, Δc)
α̂ coefficients passed to KCF detector (ROM load)
Filter α̂ (preloaded in ROM)
Initial target position (row, col)
Refined displacement (Δrow, Δcol)
Used: once Complexity: O(N² log N)
Used: Frame 2 only ⚠ Slower — O(MN log MN)
Used: every frame ✓ Fast — ≈193 µs @ 100 MHz
Trade-off: NCC provides a highly accurate, illumination-robust initial position but is expensive per frame. KCF runs in O(N²log N) — an order of magnitude faster — but requires NCC seeding. Once seeded, KCF tracks in real-time every frame.